## Slide 1: Drawbacks of Combinational circuits
If you need to design a system that stores and uses previous input and output, then we can not use a combinational circuit because it doesn’t have capability to store any state or depend clock or and time.
For these properties you can use Sequential circuits.

## Slide 2
Sequential logic is a type of logic circuit whose output depends not only on the present value of its input signals but on the sequence of past inputs, the input history as well.
Types of Sequential Circuits
  Asynchronous sequential circuits
    some or all the outputs of a sequential circuit do not change affect with respect to active transition of clock signal
  Synchronous sequential circuits
    all the outputs of a sequential circuit change affect with respect to active transition of clock signal.

## Slide 3: Memory Element
A memory stores data – usually one bit per element
A snapshot of the memory is called the state
A one bit memory is often called a bistable, i.e., it has 2 stable internal states
Flip-flops and latches are particular implementations of bistables

## Slide 4
Asynchronous
  Element delay determines speed
  Basic elements are Latches.
Synchronous
  Clock frequency (1GHz, 2GHz,etc.) -> speed
  Basic elements are Flip Flops

## Slide 5
Clock Signal and Triggering
  Clock signal
    Clock signal is a periodic signal and its ON time and OFF time need not be the same. We can represent the clock signal as a square wave, when both its ON time and OFF time are same.
    The time period will be equal to sum of ON time and OFF time.
    The reciprocal of the time period of clock signal is known as the frequency of the clock signal.

## Slide 6
Types of Triggering
  Level triggering
    Positive level triggering
    Negative level triggering
  Edge triggering
    Positive edge triggering
    Negative edge triggering

## Slide 7
Latches operate with enable signal, which is level sensitive. Whereas, flip-flops are edge sensitive.

## Slide 8
SR latch
  Q(t+1)(Q(t), S, R)
  SR Latch with NAND implementation

## Slide 9
D Latch

## Slide 10
Flip Flops

## Slide 11
Edge-Triggered D Flip-Flop
From Latches:
Master-Slave Flip-Flop
-ve edge triggered.
  f = 1/T

## Slide 12
JK Flip-Flops (from D FF)
  Input Eq: D = JQ’ + K’Q
  Characteristic Equation
    Q(t+1) = D
      = JQ’+K’Q(t)
  Characteristic Table

## Slide 13
T Flip-Flop (from D or JK FFs)
  Input Equation : D = T ⊕ Q
  Characteristic equation
    Q(t+1) = D
    = T ⊕ Q(t)

## Slide 14
D-FF with asynchronous reset

## Slide 15: Analysis and Design
To design of Sequential circuits, the procedure involves the following steps:
  Derive the state table and state equations.
  Derive the state diagram using the state table.
  Reduce states using state reduction technique.
  Verify the number of Flip-Flops and type of Flip-Flop to be used.
  Derive the excitation equations using the excitation table.
  Derive the output function and the Flip-Flop input functions.
  Derive the logic functions or equation for each output variable.
  Draw the required logic diagram.

## Slide 16
Analysis of Clocked Sequential Circuits (Synchronous Circuits)
Represents in:
. Circuit drawing
. Equation (algebraic expression, state equation, transition equation).
. Table (state table, transition table))
same as truth table,
characteristic table,
functional table
. State diagram (Finite State
Machine(FSM), transition
diagram)
. Timing diagram.

## Slide 17
Analysis with D FF

## Slide 18
Example

## Slide 19
Analysis with JK FF

## Slide 20
Analysis with T FF

## Slide 21
State Reduction and Assignments

## Slide 22
Flip-Flop Excitation Tables (inverse function)

## Slide 23
Ex: Detect 3 ones in row (overlap)

## Slide 24
Using a T FF, design a circuit that counts from 0 to 7 compare to D and JK

## Slide 25
Using a T FF, design a circuit that counts from 4 to 4 and check for unused states