## Slide 1: Counters
A special type of sequential circuit used to count the pulse is known as a counter, or a collection of flip flops where the clock signal is applied is known as counters.
Counters are of 3 types, namely:
  Asynchronous/synchronous
  Single and Multi-mode
  Modulus counter.

## Slide 2
Counters
  Synchronous
    Different FF triggered with different clock.
    Faster
    Not produce decoding errors.
    Also called parallel counter
    Variable count sequence
    Ex: Ring counter, Johnson counter
    Low propagation delay
  Asynchronous
    All FF are triggered with same clock simultaneously.
    Slower
    Produce decoding errors
    Also called serial counter
    Fixed count sequence
    Ex: Ripple, Up/Down counter
    High propagation delay

## Slide 3
Asynchronous counter
  The Asynchronous counter is also known as the ripple counter.
  Ex 2-bit Asynchronous counter in which we used two T flip-flops. The external clock pass to the clock input of the first flip flop, i.e., FF-A and its output, i.e., is passed to clock input of the next flip flop, i.e., FF-B.

## Slide 4
Synchronous Counter
  In the Asynchronous counter, the present counter's output passes to the input of the next counter. So, the counters are connected like a chain. The drawback of this system is that it creates the counting delay, and the propagation delay also occurs during the counting stage. The synchronous counter is designed to remove this drawback.
  Ex: A 2-bit synchronous counter in which the inputs of the first flip flop, i.e., FF-A, are set to 1. So, the first flip flop will work as a toggle flip-flop. The output of the first flip flop is passed to both the inputs of the next JK flip flop.

## Slide 6: Synchronous Counter
Binary Counter

## Slide 7
Up-down Binary Counter

## Slide 8
BCD Counter

## Slide 9
Binary Counter with parallel Load

## Slide 10
Design a BCD Counter using the Binary Counter with parallel load

## Slide 11
Designing procedure of Synchronous Mod-N Counters
  Step-1: Determine the number of flip-flops.
    The number of flip-flops required to design a mod-N synchronous counter can be determined by using the equation 2n >= N, where n is no. of flip-flops and N is Mod number.
  Step-2: Determine the type of flip-flop required ( JK, D, or T flip-flops.)
  Step-3: Draw the state diagram which demonstrates the states which the counter undergoes.
  Step-4: Using the excitation table of the flip-flop, obtain the flip-flop inputs for each state which were obtained in the second step, and enter them in a table. The flip-flop inputs, that are capable of producing the next state of the counter from the present state, are entered in the table.
  Step-5: Make a K-Map for each input combination and simplify it to obtain the minimal Boolean expression for each flip-flop input.
  Step-6: Using the Boolean expressions obtained in step 5, draw the required counter circuit by connecting the flip-flops and other gates as per the obtained Boolean expression.

## Slide 12
Using a T FF, design a circuit that counts from 0 to 7 compare to D and JK

## Slide 15
Ripple Counters
  Binary Ripple Counter

## Slide 17
BCD Ripple Counter

## Slide 19
Ring counter is a typical application of Shift resister. Ring counter is almost same as the shift counter. The only change is that the output of the last flip-flop is connected to the input of the first flip-flop in case of ring counter but in case of shift resister it is taken as output. Except this all the other things are same.
  No. of states in Ring counter = No. of flip-flop used
  Two types of Ring Counter:
    1. Straight ring counter or One-hot counter

## Slide 20
2. Twisted ring or switch-tail ring or walking ring or Johnson or creeping or mobile counter

## Slide 21
Ring Counters

## Slide 22
Johnson Counters

## Slide 23
Advantages of Johnson counter:
  The Johnson counter has same number of flip flop but it can count twice the number of states the ring counter can count.
  It can be implemented using D and JK flip flop.
  Johnson ring counter is used to count the data in a continuous loop.
  Johnson counter is a self-decoding circuit.
Disadvantages of Johnson counter:
  Johnson counter doesn’t count in a binary sequence.
  In Johnson counter more number of states remain unutilized than the number of states being utilized.
  The number of flip flops needed is one half the number of timing signals.
  It can be constructed for any number of timing sequence.
Applications of Johnson counter:
  Johnson counter is used as a synchronous decade counter or divider circuit.
  It is used in hardware logic design to create complicated Finite states machine. ex: ASIC and FPGA design.
  The 3 stage Johnson counter is used as a 3 phase square wave generator which produces 1200 phase shift.
  It is used to divide the frequency of the clock signal by varying their feedback.

## Slide 25: Registers
A Register is a collection of flip flops. A flip flop is used to store single bit digital data. For storing a large number of bits, the storage capacity is increased by grouping more than one flip flops. If we want to store an n-bit word, we have to use an n-bit register containing n number of flip flops.
The register is used in the CPU to perform different types of operations.
Fetch:
  To take the instructions given by the users.
  To fetch the instruction stored into the main memory.
Decode:
  To interpret the instructions.
  To decode the instructions.
Execute
  To store the result produced by the CPU into the memory.
  Results is displayed on the user screen.

## Slide 26: Registers(n-bits, with parallel load)

## Slide 27
Shift Registers

## Slide 28
Serial Transfer

## Slide 29
Serial Adder

## Slide 31
Universal Shift Register

## Slide 32
A synchronous sequential circuit is also called as Finite State Machine FSM, if it has finite number of states.
There are two types of FSMs.
  Mealy State Machine
    outputs depend on both present inputs & present states
  Moore State Machine
    outputs depend only on present states

## Slide 33
FSM

## Slide 34
FSM and Languages

## Slide 35
A sequence detector is a sequential state machine that takes an input string of bits and generates an output 1 whenever the target sequence has been detected.
Sequence detector is of two types:
  Overlapping
    the last bit of one sequence becomes the first bit of the next sequence.
  Non overlapping
    the last bit of one sequence does not become the first bit of the next sequence

## Slide 36
Detect 3 ones in a row (overlap)

## Slide 37
Detect 3 ones in row (with/without overlap) both Moore and Mealy

## Slide 38
Ex Detect 0101 with/without overlap